## Slide 1: Robot Design for Stair Climbing
Lisa-Sophie Baier
Hanane Lotf
Svetlana Shevchenko

## Slide 2: Given Requirements
Maximum mass: mass = 2000g = 2.0kg
Nominal speed: v = 350mm/s = 0.35m/s
Footprint: circular, diameter D = 50cm
Stair height: h = 2.5cm = 0.025m
Minimum runtime: t = 15min = 0.25h
PCB reserved volume: 150 × 150 × 100mm^3
Visual feedback: ≥ 300 lumen
Circular footprint: 50–60 cm
Must climb 5 stairs

## Slide 3: Climbing Force Derivation
The wheel rotates about the corner of the step
The contact force Fc at the pivot does not create any torque
The applied horizontal force F acts at the wheel center

## Slide 4: Required Wheel Torque

## Slide 5: Wheel Angular Velocity, Battery Sizing

## Slide 6: PCB Design
Stair-Climbing Robot: Electronics and PCB

## Slide 7: PCB Overview: 4-Block Architecture
Board: 100 x 80 mm
Block 1 — Power Supply: LM2596, 12V→5V
Block 2 — Motor Driver: L298N, dual H-bridge
Block 3 — Microcontroller: ESP32-C3
Block 4 — LED Lighting: separate sub-PCB, 400lm
Fig. 1 — Main PCB layout, 100 x 80 mm, KiCad

## Slide 8: Block 1 & 2 : Power Supply and Motor Driver
Buck converter (U3):steps down 12V to 5V
Schottky Diode (D9): prevents voltage spikes
Inductor (L1): For energy storage
Screw terminal (J1): 12V battery input connector
Capacitors (C1,C2): Input and output filters
Motor Driver:
L298N (U2): Controls direction and speed of both drive motors using signals from the ESP32.
Motor connectors (J2,J3): Left and right motor outputs
Flyback diodes (D5-D13): they catch voltage spikes from motor back-EMF
Fig. 3 — Block 2: L298N motor driver
Fig. 2 — Block 1: LM2596 power supply
Power Supply:

## Slide 9: Block 3 & 4: Microcontroller, Sensors and LEDs
Microcontroller and Sensor Interface:
ESP32-C3 (U1): Main microcontroller. Runs navigation firmware, controls motors, reads sensors, and drives LEDs
TCRT5000 (J4):3-pin header for IR sensor for line tracking
HC-SR04 (J5): 4-pin header for ultrasonic sensor for obstacle detection
Transistor 2N2219 (Q1): LED switching transistor. Controlled by ESP32 IO9
LED Lighting:
Connectors (J6,J7): LED_IN & LED_OUT 2-pin connectors to power LEDs with 12V via cable
LEDs (D1-D4): Each LED provides 100 lm/w
Resistors (R1,R2): Limit current to 300 mA per LED
Fig. 4 — Block 3: Sensor interface
Fig. 5 — Block 4: LED sub-PCB

## Slide 10: PCB Requirements
PCB fits in chassis: 100x100x80mm within reserved volume
Stair climbing: L298N supports 1.84Nm torque
15 min runtime: 1.09Ah battery
Line tracking + remote control: TCRT5000 + ESP32 Wi-Fi
400lm visual feedback: exceeds 300lm requirement
Remote Control: Blynk app via ESP32 Wi-Fi, no extra hardware needed.

## Slide 11: Design Requirements
Circular footprint: 50–60 cm
Maximum weight: 2000 g
Must climb 5 stairs
Step height: 25 mm
Designed in Autodesk Fusion

## Slide 12: Final CAD Design
Circular ring frame
Central core for electronics and battery
Two driven front wheels
Fixed passive rear wheel
Custom TPU tires

## Slide 13: Components
Core
Ring
Lid
Tires+ axis
Main PCB + LED PCB
2x Motors
Ultrasonic sensor
IR sensor Array
Battery
M2 Inserts and Screws

## Slide 14: Weight-Saving Design Decisions
Big in size
Ring structure instead of solid circular base
Open core with ribs for stiffness
Fixed rear wheel

## Slide 15: Wheels
custom TPU tires
conneced to motor via 3d-printed axis

## Slide 16: Requirement Check / Conclusion
✓ Footprint: 500 mm diameter
✓ Weight: 1405 g → below 2000 g
✓ Stair climbing: 25 mm step verified
✓ Design priority: low weight + simple mechanics